## Slide 1: Scattering models in fisheries acoustics
Sven Gastauer, 2020
Scipps Institution of Oceanography, University of California San Diego
sgastauer@ucsd.edu

## Slide 2: What will we discuss?
Why use scattering models?
What are the main contributors to the scattering?
What models are commonly used?
How to get model input parameters?
How to use ZooscatR for model simulations
How to exploit scattering properties to get size estimates of fish?

## Slide 3: Why and what to model?

## Slide 4
What a mess!
Can we make some sense out of this?

## Slide 6
What are main contributors to the scattering?
Main factors influencing target strength:
Echosounder properties -> Frequency
Material properties -> Acoustic impedance, dictated by the density and sound speed contrast
Behaviour -> Orientation (incident angle) of the target
Morphology and Physiology -> Size and shape of the target
Varying g and h
Varying L/a (fatness)

## Slide 7: Demonstration Calibration Sphere in R

## Slide 8
Approximate models
Kirchhoff Ray, Distorted Wave Born Approximation, DCM,…
Advantages:
arbitrary scattering surface & orientation
can be (very) fast & simple
Disadvantages:
model specific restrictions to frequency and material properties range validity
excludes diffraction effects or internal structure
multi-body scattering is additive
Numerical models
Finite/Boundary Element Methods,…
Advantages:
arbitrary shapes/internal structures,
include diffraction/FSI
arbitrary materials and frequencies
include interaction effects between multiple bodies
Disadvantages:
computationally expensive and complex models
Three major categories of scattering models
Analytic/semi-analytic models
for simple geometric shapes (e.g. spheres, prolate spheroid,…).
Advantages:
exact
Some are fast
Some are not restricted in frequency/material properties
Disadvantages:
cannot model realistic objects
assume a single scattering object
Can be slow and restrictive in terms of material properties and frequencies

## Slide 9
https://github.com/AustralianAntarcticDivision/ZooScatR

## Slide 10: Using ZooScatR – the easy way
Getting help through Vignettes or function descriptions
Run the shiny web app
Installing the package

## Slide 11
DWBA Model
k = wave number
= wave length [m]
f = frequency [Hz]
c = ambient sound speed [m/s]
Frequency and ambient sound speed dependence
related to compressibility
g=ρb/ρs and h =cb/cs
Body properties/condition
is the position vector along the body axis
Phase Term
v is the integration volume of the body

## Slide 12: Live Demonstration ZooScatR….. Demonstrate the influence of g and h and size on spheres, prolate spheroids and krill

## Slide 13: Get model input parameters

## Slide 14: Shape demo

## Slide 15
CT Scans for meshes

## Slide 16
CT Scans for meshes

## Slide 17: OCT
Bellini N, Cox MJ, Harper DJ, Stott SR, Ashok PC, et al. (2014) The Application of Optical Coherence Tomography to Image Subsurface Tissue Structure of Antarctic Krill Euphausia superba. PLOS ONE 9(10): e110367. https://doi.org/10.1371/journal.pone.0110367
https://journals.plos.org/plosone/article?id=10.1371/journal.pone.0110367

## Slide 18: Camera or photo recordings
Contours from X-Rays

## Slide 19: Stereo camera recordings
Background removed, smoothed,...
Blob and contours detected

## Slide 20
Background removed and filtered
Right frame
Combined Disparity map
Original recording
Right frame
Y-axis
Z-axis
2D projection
Shape for model
Tapering
Model output

## Slide 22: Size / g&h demo

## Slide 23: Measuring density and sound speed contrast
g = density contrast | h = sound speed contrast

## Slide 24: Acoustic subsystem
Animal compartment
Pulser
Transmitter (transducer 1)
Receiver (transducer 2)
Amplification
Data reception
Computer
Pulse generations
Seawater
Holes (let water enter)
Pulser/Receiver
Oscilloscope

## Slide 25: Density measurements
2 fluid solution to get the density contrast
Measuring the densities of the fluids separately and combined
Measuring the weight of the compartment with and without animals and liquids
-> Resolve equations to get density contrast h

## Slide 26: Krill survey 2019
Synoptic krill survey 2019:
7 vessels covering total of over 15,822 nm
Trained personnel aboard:
4,562 nm by Norwegian vessel
1,119.9 nm Chinese FV
1059.7 nm by Aker

## Slide 27: Sizing targets

## Slide 28
Scattering by a fluid-like sphere
Size dependent periodicity, condition dependent amplitude
Good results for a signal to Noise ratio ~0
TS at different sizes with varying g and h
Target detection at accuracy at different Signal to Noise Ratios

## Slide 29
 | Measured |  |  | Acoustics |  |  |  | 
ID | Length | Width | L/a | N | Δf | sd Δf | Width | sd Width
1.0 | 23.1 | 4.3 | 10.7 | 25.0 | 18.7 | 0.16 | 4.1 | 0.04
2.0 | 22.0 | 4.0 | 11.0 | 38.0 | 18.6 | 0.15 | 4.1 | 0.03
3.0 | 23.1 | 4.1 | 11.3 | 42.0 | 18.6 | 0.13 | 4.1 | 0.03
4.0 | 24.6 | 4.2 | 11.8 | 43.0 | 19.1 | 1.42 | 4.2 | 0.25

## Slide 30: Scattering by rotated prolate spheroids
0°
30°
60°
90°

## Slide 31: In situ measurements – getting height of the fish

## Slide 32: In situ measurements – getting orientation of the fish
Echoview track direction
(Vertical direction first to last point in track)
Tilt angle derived from broadband data

## Slide 33: Conclusion and outlook
Scattering models are not reality
Scattering models can help us to improve our understanding of the complex reality
Scattering models look scary at first but can be used by a broad audience with some background knowledge
ICES WGFAST will host a workshop next year to work on opensource, easy to use, standardized scattering models

## Slide 34: Thank You!